## Slide 1
Debugger
C/C++
IEC
Java
python
Simulink/LabView
JavaScript
CANOpen
TCP/IP
UDP
Modbus
OPC UA
EAP(Beckhoff)
Linux | RT Linux | Linux+Xenomai | ucLinux |
Win CE | Win 10 | Vxworks（Reworks）| QNX
x86
ARM
A8/A9/
A53/M7
MIPS
(龙芯)
EtherCAT
Ethernet
profinet
profibus
CAN
RS485/232
KNX
编程语言
通讯协议
操作系统
硬件平台
现场总线
组件模型
基于类ObjectServer的动态加载、卸载和更新
组件加载签名认证
变量和数据区域的（跨RTE）映射
（跨RTE）接口调用
DDS消息总线（路由）
可靠性（冗余和高可用）

## Slide 2
组件虚拟总线
Device 1
Device 2
Device 3
Device 0
Component Manager
Component Manager
Component Manager
Component Manager
Hardware
RTOS
Hardware
RTOS
Hardware
RTOS
Hardware
RTOS
Resource constraint
共享内存
UDP
1.元模型和组件分类
嵌套、系统功能、调用方式（周期）
2.端口分类
根据交互方式，require/provide，
memory mapping，non-functional
3.组件资源描述
（静态）内存分配，特定IO等
4.组件安全状态机
组件行为协议，接口绑定委托检查等
5.组件生命周期管理
基于Component Manager的组件加载、卸载、动态更新
6.组件间通信
所有组件面向虚拟总线构建交互端口，根据位置选择最优通信路径
7.高可用
计算节点故障时的组件迁移（冗余）方案

## Slide 3
组件虚拟总线
计算节点 1
计算节点 2
计算节点 3
Component Manager
Component Manager
Component Manager
Hardware
RTOS
Hardware
RTOS
Hardware
RTOS
硬件
约束
共享内存
UDP

## Slide 4
组件分类
Composite Components：根据是否有子组件分类
Basic Components ：系统基础功能组件
Passive Components：被动调用还是周期执行并能创建线程（task）
Specific IO Components
DDS Components

## Slide 6
Component B
Input Area
Topic
Output Area
Topic
Component A
Cyclic
Task
input
output
input
output
Cyclic
Task
Component A
Component B
Data Flow
Topic
filter
Component A
Component B
Event Trigger
Topic
sender
receiver
Component C
trigger
listener
listener
IDL
Component A
filter
Component B
Request
Topic
Reply
Topic
requester
replier

## Slide 7
CMC
Component
Manager
Component
BSC
Basic
Service
Component
PAC
Pluggable
Application
Component
Manager Channel
Application Channel
Local Channel
Pre-defined

## Slide 8
Hardware
RTOS
Component
Manager
Ethernet Adapter
RT-task Server
IO Manager
Context 1
Context 2
Context 3
Context 1
Context 2
Context 3
现场总线
DDS port
Cyclic port
Common port
Control port

## Slide 9
action保留，资源释放
INIT
PREOP
SAFEOP
由于一个module被创建后立刻在IP过程中进行实例化，所以一般module不会停在INIT状态
IP
在Objectserver中注册
实例化，参数初始化
分配系统资源（内存等）
所有module创建完成，但模块之间的还未建立任何连接
PS
通过objectserver获取其他module的objectID等信息并建立连接
此过程由configurator触发并可由父模块进行传参
SO
OP
进入real-time context
module之间可以互相注册并申请资源（如实时task）
action保留，资源释放
action保留，资源释放，
在ObjectServer中删了自己
CH_INIT_SYSTEM：初始化系统组件
CH_INIT：初始化其他组件和其局部变量
CH_INIT2：初始化完毕，可使用接口，如创建event
CH_INIT3：初始化完毕，可使用接口，如event注册
CH_INIT_SYSTEM_TASKS：启动task（IEC应用必要的）
CH_INIT_TASKS：启动其余task（引导项和PLC task）
CH_INIT_COMM：启动level7 server和通信
CH_INIT_FINISHED：启动完成
CH_COMM_CYCLE (hook)：operating mode
CH_EXIT_COMM：所有level7 server关闭通信通道
CH_EXIT_TASKS：除了IEC应用所需task，终止其他task
CH_EXIT_SYSTEM_TASKS：终止所有task
CH_EXIT3：移除注册和组件间依赖关系
CH_EXIT2：释放在CH_INIT2中所占用的局部资源
CH_EXIT：释放所有局部资源并析构(deinitialize)组件
CH_EXIT _SYSTEM2 ：析构(deinitialize)系统组件
CH_EXIT _SYSTEM：析构系统组件随后卸载组件

## Slide 10
App
Runtime system
TC
OS

## Slide 11
Type-Prototype Pattern

## Slide 13
Life Cycle
Taxonomy
Design Phase
Deployment Phase
Run-time Phase
Syntax
Semantics
Composition
Object−oriented Programming Languages
Programming Languages with IDL mappings
Architecture Description Languages
Classes
Objects
Architectural Units

## Slide 14
Port Instance
Port
Interface
Service
Require port
Provide port
Require/Provide port
Passive
Periodic
 | Synchronous | Asynchronous
Control-based | Request-reply interface | Event-trigger interface
Data-based | Cyclic synchronous interface | Send-receive interface
 | Intra-container port binding | Inter-container port binding
request-reply interface |  | 
send-receive interface |  | 
cyclic synchronous interface |  | 
event-trigger interface |  | 

## Slide 15
Design
Deployment
Run-time
Builder
Repository
Assembler
Distributed RTE
A
B
C
D
CD
A
A
B
B
D
CD
C
D
insA
insB
insB
insD
insCD
deposit
compile
retrieve
deposit
instantiate
A
B
insA
A
A
component
component(binary)
component
instance
component container
design phase composition operator
(composite)
deployment phase composition operator
(intra-container assemble)
run-time phase composition operator
(inter-container/run-time assemble)

## Slide 16
Builder
(Vendor)
Repository
(Vendor)
Object
Repository
(OEM)
A
B
A
A
B
C
D
CD
CD
C
D
deposit
insA
insB
insB
insCD
deposit
retrieve
compile
instantiate
component
component
(binary)
component
instance
instancebus
A
A
insA
Design Phase
Deployment Phase
composite
Distributed
RTE
E
insE
insA’
update
Run-time Phase
insF
unload
load
Modeler
(OEM)
CTR.xml
Software
Architecture
Hardware
Architecture
assign
merge
IAD.xml
CRD: Component Template Repository
IAD : Instance Architecture Description
Third-party
Software

## Slide 17
State Machine
Service
Function
Event
Application
Composite
Atomic
DataArea
Assemble
Delegate
Delegate

## Slide 19
Component Type
Atomic Component Type
Composite Component Type
Atomic/Composite Component Type References
State Machine
Service
AC Type Reference
Interfaces

## Slide 20
MotionControl
AC_Instance
CoETransport_1
AC_Instance
R_MoveAxisbyPos_1
P_MoveAxisbyPos
OSAI Connection
P_ GetAxisPos
CoETransport_2
AC_Instance
P_MoveAxisbyPos
P_ GetAxisPos
R_ GetAxisPos _1
R_MoveAxisbyPos_2
R_ GetAxisPos _2
Visualization
AC_Instance
PR_AxisPosSync
NCControl
AC_Instance
PR_AxisPosSync
P_SendSignal
R_ SendSignalHandler

## Slide 21
P_ConfigDC
Binding
Delegation
CoETransport
Composite_AC_Type
CANOpenProtocolSuppport
Atomic_AC_Type_Ref
EtherCATMaster
Atomic_AC_Type_Ref
P_ECConfigDC
P_WriteSDO
R_WriteSDO
P_ReadSDO
R_ReadSDO
P_ConfigOPMode
P_ConfigMode
R_ECSend
R_ECReceive
R_EthSend
R_EthReceive
P_SetPos
P_LifeCycle
P_MoveAxisbyPos
P_ GetAxisPos
P_GetPos

## Slide 22
CM
BC
AC
Hardware
OS
OS
Hardware
Container A
Container B
Container C
Node 1
Node 2
CM
BC
AC
CM
BC
AC
intra-node communication
handled by middleware
(shared memory)
inter-node communication
handled by middleware
(field bus)
Dynamic linking
CM : component manager；BC : basic component；AC : application component

## Slide 23
IAM : Instance Adaption Manager
OSAS : Operating System Abstraction Server
PAC : Pluggable Application Component
LAC : Low-equipped Application Component
Node A
Node B
Node C
Hardware (MCU)
Hardware
Hardware
Low-level RTE
OS (real-time)
OS
OSAS
IAM
RT-Task
Manager
OSAS
IAM
PAC
LAC
Other run-time supports
or specific drivers
Intra-node communication
via shared memory
Real-time task
Service
Inter-node communication
via field bus
Run-time
Support
Layer
Dynamic
Instance
Space
UDB
UDB : Unified Dynamic Bus

## Slide 24
CAM : Component Adaption Manager
OSAS : Operating System Abstraction Server
PAC : Pluggable Application Component
LAC : Low-equipped Application Component
Node A
Node B
Node C
Hardware (MCU)
Hardware
Hardware
Low-level RTE
OS (real-time)
OS
OSAS
CAM
RT-Task
Manager
OSAS
CAM
PAC
LAC
Other run-time supports
or specific drivers
Intra-node communication
via shared memory
Real-time task
Service
Inter-node communication
via field bus
Run-time
Infrastr-ucture
Layer
Contain-erized
Instance
Layer
UDB
UDB : Unified Dynamic Bus

## Slide 25
Hardware
Low-Level Runtime(OS)
Low-Level Runtime(OS)
Hardware
C
Python
Java
C
IEC
C
C++
intra-node communication
handled by middleware
(shared memory)
inter-node communication
handled by middleware
(field bus)
Node 2
Node 1
IoC Manager
IoC Manager

## Slide 26
CANopen
Modbus
IEC
EtherCAT
CANopen
EtherCAT
Algo
HMI

## Slide 27
Routing
DCPS Manager
Request
Topic
Reply
Topic
Interface
Router
Message
Queue
Manager
Shared Memory
Manager
Event
Manager
Local
Routing
Remote
Routing
Input Area
Topic
Output Area
Topic
Data Flow
Topic
Event Trigger
Topic

## Slide 28
组件实例化，参数初始化；组件通过Dynamic Linking加载，并在Component Manager注册其提供的interface
查询Component Manager，获取所需的interface，并建立组件间路由连接（Local routing, DCPS writer/reader）
Periodic service绑定task，并开始运行。
停止接收新的调用和通信，等待当前调用执行完成并返回。
调用执行完成，释放资源，解绑task。
注销Component Manager中注册的Interface，卸载组件。
阻塞新的调用和通信，等待当前调用执行完成并返回。
解绑task，更换新的component实例，将之前的引用重定向至新版本的组件，并重新建立连接
唤醒步骤⑦中阻塞的调用和通信，重新绑定task 并开始运行。
LOADED
INIT
READY
BLOCKED
ACTIVE
DEACTIVE
DELETED
1
8
7
4
5
2
3
6
UPDATED
9
PARALLEL

## Slide 29
Node A
Node B
Subscriber
Publisher
Subscriber
Publisher
Subscriber
Publisher
Subscriber
Publisher
Subscriber
Publisher
Subscriber
Publisher
Node C
Subscriber
Publisher
  Channel 1 (Topic:1-A,1-B)
Channel 2 (Topic:2-A)
Channel 3 (Topic:3-A,3-B)
DCPS Manager(Basic Component)
DCPS Manager
DCPS Manager
组件虚拟总线
Data reader
Data writer
Topic 3-A
Topic 3-A
Topic 3-B
Topic 3-B
Topic 3-B
Topic 1-A
Topic 1-A
Topic 1-B
Topic 1-B
Topic 2-A
Topic 2-A
Topic 3-A
Topic 3-B
Topic 2-A
Topic 3-A

## Slide 30
 | DR | RR | CS | DC | CP | CR
JavaBeans
EJB
COM
.NET
CCM
Koala
SOFA
KobrA
ADLs
UML2.0
AUTOSAR
PECOS(8)
Pin
Fractal
µ-Kevoree(5)
TDL(9)
FORMULA(10)
Rubus(12)
IEC 61449(14)
ICSCM