## Slide 1
A Pluggable Component Model
For Industrial Control System
暂定名称：ICSCM

## Slide 2
Introduction
Industrial Control System(ICS)
  一种分布式嵌入式系统，广泛应用于制造业工厂、核电站。
  Safety-critical的应用场景使其对实时性和可靠性等具有较高要求
  随着ICS的规模地扩大和复杂性不断提高，ICS的开发过程也需要科学高效的软件工程方法的指引。
Component-based software engineering
  基于组件的软件工程使用组件化的开发方法，旨在提升系统的复用性以减少开发流程开销。
  组件模型在通用软件领域举例：UML，JavaBean/EJB，COM/DCOM，Corba
  基于组件模型技术的嵌入式系统开发在各自领域也获得了成功：AutoSAR，Rubus

## Slide 3
Introduction
ICSCM
  将组件模型技术应用于ICS，因其特殊性面临的挑战。
  提出ICSCM，一种灵活的嵌入式组件模型，具有如下特性
    Design-time完备的组件分类，端口分类，组装方法，meta-model。
    组件面向虚拟数据总线(VirtualDataBus)开发，大部分组件具有locationindependence。
    基于publish/subscribe模型的组件间通信，实现多种communicationpattern，和自适应的通信路径选择，组件间通信通过指定channel进行功能性地隔离。
    基于componentmanager的组件加载、卸载，结合组件状态机实现运行时模型的动态更新。
    其他（待定）
论文架构

## Slide 4
RelatedWorks
通用软件系统组件模型
  列举JavaBean/EJB，COM/DCOM，Corba，.NET
  突出SOFA2和其提出的关于academic + industrial，multi-communication model，dynamic reconfiguration，control part的观点。
嵌入式系统组件模型
  列举PECOS，KOALA，ROBOCOP
  突出Rubus在模型定义方面对时间约束、资源约束做出的工作
  µ-Kevoree作为最新的有关组件模型的工作，提出了在组件模型Dynamic Adaptation方面的四层概念，在组件模型动态适应能力方面做出了改进。
  AutoSAR作为车载控制系统标准，其组件模型基于VFB开发具有易组装、portability、标准化等优势。

## Slide 5
Preliminary
ICS
  ICS包括用于操作和自动化工业过程的设备，系统，网络和控制，用于大部分工业部门和基础设施，如制造，运输，能源等。
  工作环境较为严苛，safety-critical，控制系统的更新需要在尽可能不停机的情况下完成。
  PLC，ICS系统的基本计算硬件，并提供传感器和执行器等IO运行过程的本地管理。
    PLC中IEC应用程序执行模式
    PLC中的其他应用
      C/C++等高级语言实现功能模块
      HMI，系统配置、诊断、错误反馈
      多种通信链路的协议栈
      机器人运动控制算法、机器视觉图像处理模块等

## Slide 6
Preliminary
Casestudy
Gateway
PC
PLC1
PLC2
EtherCAT/CANBus
工件加工
流水线
六轴
机械臂

## Slide 7
Preliminary
Publish/Subscribemodel
  发布订阅基本模型和概念
  支持一对多、多对多通信
  发布者和订阅者无需互相知晓，只需按一定数据类型往指定的topic发布或者订阅数据，以此为基础可实现可插拔的组件间通信。
DDS
  采用DDS作为组件通信的中间件技术。
  DDS具有较高的实时性，以及多种Qos策略保证数据传输的可靠性。
  数据传递双方充分解耦，结合其对pub/sub的发现机制，有助于我们实现可插拔的组件。
publisher
publisher
subscriber
subscriber
subscriber
Topic

## Slide 8
ICSCM Component Model
CMC
Component
Manager
Component
BSC
Basic
Service
Component
PAC
Pluggable
Application
Component
组件分类
Attributes
isPassive
isIOspecific
isComposite
Meta-model

## Slide 9
ICSCM Component Model
Publish/Subscribe pattern
Subscriber
Publisher
Component
Component
Topic A
Topic B
Group
Node A
Node B
Subscriber
Publisher
Subscriber
Publisher
Subscriber
Publisher
Subscriber
Publisher
Subscriber
Publisher
Subscriber
Publisher
Node C
Subscriber
Publisher
  Channel 1 (Topic:1-A,1-B)
Channel 2 (Topic:2-A)
Channel 3 (Topic:3-A,3-B)
DCPS Manager(Basic Component)
DCPS Manager
DCPS Manager
组件虚拟总线
Data reader
Data writer
Topic 3-A
Topic 3-A
Topic 3-B
Topic 3-B
Topic 3-B
Topic 1-A
Topic 1-A
Topic 1-B
Topic 1-B
Topic 2-A
Topic 2-A
Topic 3-A
Topic 3-B
Topic 2-A
Topic 3-A

## Slide 10
Communication pattern/port
ICSCM Component Model
IDL
Component A
filter
Component B
Request
Topic
Reply
Topic
requester
replier
Component B
Input Area
Topic
Output Area
Topic
Component A
Cyclic
Task
input
output
input
output
Cyclic
Task
Component A
Component B
Data Flow
Topic
filter
sender
receiver
Component A
Component B
Event Trigger
Topic
Component C
trigger
listener
listener

## Slide 11
CMC
Component
Manager
Component
BSC
Basic
Service
Component
PAC
Pluggable
Application
Component
Manager Channel
Application Channel
Local Channel
Pre-defined
ICSCM Component Model

## Slide 12
ICSCM Component Model
Component
Registry
INIT
PREOP
SAFEOP
OP
Local Channel